## Slide 1
Task Switching with the i960® Microprocessor
Developed by: Tom Johnson
Reviewed by:

## Slide 2
Outline
Call/Return Mechanism
Processor State
Interrupt Record
Recipe
Code Example

## Slide 3
Call/Return Mechanism
Memory/Stack Growth
g0
...
fp (g15)
r15
...
rip (r2), back to main
sp (r1)
pfp (r0)
Previous Frame
int foo()
{
int i = 0;
int j = 1;
return i + j;
}
void main()
{
int k;
k = foo();
}
pfp (r0)
sp (r1)
...
r15
k
...
r15
i
j
pfp (r0)
sp (r1)
Current Frame
Next Frame
Goes Here
Current Frame
External Memory

## Slide 4
Call/Return Mechanism
Each call allocates new set of local registers
Each return deallocates current set of local registers
Local register sets (frames) stored in on-chip register cache
Register cache not automatically flushed

## Slide 5
Processor State
Process Controls (PC)
Arithmetic Controls (AC)
Trace Controls (TC, optional)
Global Registers (g0 - g14)
  g15 takes care of itself
Local register frames stored in on-chip register cache

## Slide 6
Interrupt Record
i960® Processors automatically save PC and AC
Interrupt Stack
(External Memory)
Optional Data
fp - 4
Interrupt Stack Start
(fp)
New Frame
Memory
Growth
fp - 8
fp - 12
fp - 16
Saved PC
Saved AC
Vector

## Slide 7
Recipe
Save PC and AC from interrupt record
Save current state of TC (optional)
Save current state of previous frame pointer (pfp)
Save current state of global registers (g0-g14)
  g15 updated by pfp upon return
Execute flushreg instruction
  flushes registers sets in register cache to external memory
Restore pfp to point to current frame of next task
Restore PC, AC, and TC (optional) for next task
  PC and AC updated by writing to interrupt record
Restore global registers for next task
Execute return instruction

## Slide 8
Code Example